## Slide 1
CACHEWISE × AGENT TRACES
CacheWise 的核心 predictor 没有稳定迁移到我们的 agent traces
论文复现 · causal progress · synthetic concurrency · task stability
一句话结论
metadata 有信号， 但收益被少数极端任务支配； 离可部署 policy 还差 task robustness 与真实 KV pressure。
+0.587 s
SWE · C100 更差
95% CI [+0.120, +1.188]
−72.299 s
TB · aggregate 更好
但 single-task fragile
+4.012 s
Timeout · delete-one 翻转
mixed-integer-programming
16 slides · 15–20 min · development-only evidence
Paper: CacheWise, arXiv:2606.16824v1 · Local evidence: analysis/results/cachewise-*20260731/

## Slide 2
PAPER PROBLEM
Coding agent 把一次用户任务变成“LLM ↔ tool”的长闭环
02
用户任务
→
LLM
→
tool
→
LLM
→
tool
tool 运行时，LLM 不占算力；但会话 KV prefix 仍驻留 GPU，等待下一轮复用
GPU HBM
多个长 session 竞争有限 KVCache
36 min
CATraces median session
tail > 2.6 h
20×
tool-triggered turns
median vs user-triggered
21×
prefill / decode ratio
vs chatbot workloads
CacheWise paper §3, Figures 2–8. Paper statistics are CATraces claims, not measurements from our traces.

## Slide 3
CORE INSIGHT
真正的 eviction 问题不是“多久”，而是“谁最晚回来”
03
memory pressure at time t
now
S₁
remaining = 2s
S₂
remaining = 40s
evict this KV
S₃
remaining = 9s
Belady-like target
j* = arg max τⱼ(t)
CacheWise 的关键简化
不必精确预测 duration；只要把“最晚回来”的 session 排到第一。
CacheWise paper §4–5.2. τ means time to next KV reuse; predictive eviction targets relative ordering.

## Slide 4
SYSTEM DESIGN
CacheWise 用两个互补机制减少 KV thrashing
04
① PREFIX-AWARE SCHEDULING
先服务需要新增 KV block 最少的 request
aᵢ(t) = dᵢ − kᵢ(t)
A
+2 blocks
B
+7 blocks
C
+4 blocks
结果：少动别人的 prefix，也近似 shortest-job-first
② PREDICTIVE EVICTION
真的要 evict 时，优先释放预计最晚复用的 KV
tool_name + tool_args + elapsed
↓
E[ remaining | survived to elapsed ]
vLLM prototype ≈2,500 Python LoC · 每 3 engine iterations 重建 eviction heap
CacheWise paper §5.1–5.3. The two mechanisms are independent in the paper ablation.

## Slide 5
NECESSARY DETAILS
Predictor 是 survival estimator，不是普通 duration regression
05
outer args
{"command":"pytest…"}
→
TF-IDF
≤5,000 terms
→
KMeans
C=20 / 50 / 100
→
history
durations in cluster
→
survive
keep D > elapsed
→
rank
max E[D−e | D>e]
小例子
cluster history: 2s, 5s, 40s, 90s
elapsed = 10s → survivors = 40, 90
prediction = mean(30, 80) = 55s remaining
BOUNDARY
论文的 tool_args = 完整外层 payload
不解析 shell AST · 不拆 pipeline · 不观察 execve child · 不使用 per-process counters
CacheWise paper §5.2 and footnotes 2–3 · analysis/offline/related-work.md, “CacheWise granularity”.

## Slide 6
CLAIM BOUNDARY
论文的 3.5× headline ≠ argument predictor 的 isolated gain
06
PAPER · FULL SYSTEM
2× H200 · Qwen2.5-Coder-32B · TP=2
• CATraces random 80/20 sessions
• 30 / 40 / 50 concurrent sessions
• prefix-aware scheduling + predictive eviction
2.7–3.5×
session time
2–2.6×
fewer evictions
≤19%
C100 isolated
OURS · PREDICTOR TRANSFER
只复现一个必要子命题
“whole args 是否比 tool-name 更会排 victim？”
• 同样的 global / tool / C20 / C50 / C100
• 同样的 conditional remaining 与 C100 primary
• 没有实际 KV capacity / eviction / JCT
如果 predictor gate 不过，就没有理由花成本做 live serving。
CacheWise paper §6, Figures 13–19. Paper leaves temporal/cross-project drift robustness to future work.

## Slide 7
DATA & SETUP
我们的 traces 保留 raw args，但物理条件与论文不同
07
corpus
fit
evaluation
tool gaps
observed ranking
SWE-ReBench
100 sessions
277 sessions
4,175 → 12,771
2,410 events · max c=2
Terminal-Bench
139 declared 136 w/ gaps
100 declared 99 w/ gaps
1,888 → 1,227
synthetic only
WE HAVE
raw outer tool args ≈0.5s causal CPU/network samples
WE DO NOT HAVE
recorded shared KV pressure actual eviction / recompute feedback
SYNTHETIC
只平移真实 trace 的到达时间 内部 gap duration 保持不变
Local artifacts: SWE/TB result.json data fields; analysis/offline/related-work.md. All corpora are development-exposed.

## Slide 8
METRIC · LOWER IS BETTER
唯一主指标：选错 victim 会损失多少“可释放时间”
08
ranking event @ t
A
actual remaining 40s
tool predicts 10s
B
actual remaining 15s
tool predicts 20s
C
actual remaining 4s
tool predicts 5s
tool chooses B
→
regret = 40 − 15 = 25s
定义
regret = max(actual remaining) − chosen actual remaining
0 = oracle choice
Δ = mean regret(candidate) − mean regret(tool)
GO only if 95% CI upper < 0
口径：hypothetical victim ordering ≠ eviction count ≠ KV bytes ≠ JCT
Local protocol: analysis/offline/related-work.md; src/tool_resource_eval/cachewise_reproduction.py::evaluate.

## Slide 9
DECISION LADDER
五个冻结实验逐步排除四种解释
09
1
SWE observed overlap
whole args?
+0.587s
NO-GO
2
causal progress
live counters?
+0.505s
NO-GO
3
SWE synthetic c32
overlap too sparse?
+1.847s
NO-GO
4
TB synthetic c32
corpus-specific?
−72.299s
FRAGILE
5
exact timeout + LOTO
simple signal stable?
+4.012s*
NO-GO
* step 5 reports the predeclared worst delete-one-task result; aggregate timeout Δ = −17.271s.
Frozen protocols and outcomes: analysis/development/research-directions-20260729.md.

## Slide 10
RESULT 1 · OBSERVED OVERLAP
SWE：argument clustering 增大 regret，主 gate 失败
10
global
0.778 s
tool
0.780 s
C20
0.857 s
C50
1.179 s
C100
1.366 s
↓ lower is better
PRIMARY C100 − tool
+0.587 s
95% CI [+0.120, +1.188]
Δ mean victim regret (s)
better
worse
rare tail dominates
top-1: 93.98% → 94.07%
p99 regret: 17.3s → 35.5s
90 choice changes: 46 help / 44 harm · harm 1,803s vs help 390s
Source: analysis/results/cachewise-swe-reproduction-20260731/result.json; tail diagnostic in analysis/offline/related-work.md.

## Slide 11
FAILURE ANALYSIS · EVIDENCE VS INFERENCE
SWE 失败不是“cluster 太小”，而是相似命令跨 repo 的尺度不同
11
OBSERVED
syntactically similar pytest / test-suite cluster
FIT cluster max
3–29s
HELD-OUT still active
108–300s
C100 predicts 0–5s remaining
tool-name predicts 20–53s
median harmful-cluster surviving support = 36 → 不是简单 singleton 问题
SUPPORTED INFERENCE
TF-IDF 识别“在跑测试”， 却看不到 suite scale、dependency/cache state、repo-specific work。
NOT TESTED
环境状态特征是否能泛化？
repo size · test inventory · dependency/cache state · process phase
不能在已暴露 fresh-277 上继续调 tokenization / support threshold。
Source: analysis/offline/related-work.md, post-result mechanism diagnostic. Top-10 task pairs explain 91.5% of harmful delta.

## Slide 12
RESULT 2 · CAUSAL PROGRESS
Progress counters 改善 MAE，却把 ranking 决策推向错误方向
12
tool
0.780 s
progress
1.284 s
↓ lower is better
progress − tool regret (s)
better
worse
point prediction
57.43→55.24
MAE improves
+26.25→−16.83
signed error flips
decision boundary
8 / 63
help / harm changes
32.9 / 1,249
help / harm seconds
OBSERVED: 71 changes都从 still-running gap 转向新到达 gap。
INFERENCE: model 对活跃长任务变得过度乐观；fit metric 与 policy utility 方向相反。
Source: analysis/results/cachewise-progress-counter-20260731/result.json. Features are causal ≈0.5s CPU/network samples.

## Slide 13
RESULT 3 · FIXED-DURATION COUNTERFACTUAL
把 concurrency 合成到 c32，SWE 仍然失败
13
task A
task B
task C
task D
arrival shifts only; each trace keeps its internal gaps + durations
32
arrival seeds
22.2
mean live sessions
36–42
max live sessions
SWE synthetic-c32
tool
57.961s
C100
59.808s
Δ +1.847s
95% CI [+1.087, +2.646]
24 harmful / 8 helpful schedules
已排除：natural SWE overlap 太稀疏
未排除：真实 contention 会改变 duration / arrival / eviction feedback。
Source: analysis/results/cachewise-swe-synthetic-c32-20260731/result.json. This is not a live concurrency experiment.

## Slide 14
RESULT 4 · CROSS-CORPUS TRANSFER
TB aggregate 反转为正，但几乎由 hdfs-deployment 扛住
14
tool
194.633 s
C100
122.334 s
↓ lower is better
C100 − tool regret (s)
better
worse
29 / 32 schedules improve
POST-HOC SENSITIVITY
remove hdfs-deployment
+26.722 s
95% CI [+17.355, +37.789] · harmful 28/32
OBSERVED
hdfs-deployment
2 × ≈600s download exec
C100 从 command text + explicit timeout=600 识别长 survivor。
C50 regret 113.224s < C100 122.334s；但 C50 不是 primary，不能事后改选。
Source: analysis/results/cachewise-tb-synthetic-c32-20260731/result.json; hdfs sensitivity in research-directions-20260729.md.

## Slide 15
RESULT 5 · EXACT-TIMEOUT LOTO
Timeout 只是 ceiling：task-stability gate 失败
15
AGGREGATE PASSES
tool 194.633s
→
timeout 177.362s
Δ -17.271s · CI [−29.739, −4.296] · 20/32 helpful
TASK STABILITY FAILS
delete mixed-integer-programming
+4.012s
仅 13/32 schedules helpful · 99 个 task 全穷举，只有这一个翻转符号
timeout = 300s
ceiling
0.1s
4s
90s
300.011s
同一个 timeout 值覆盖多个数量级的实际 work。
OBSERVED
600s signature 提供最大 aggregate benefit； 300s signature 若没有这个跑满 300s 的 solver call，则净有害。
Source: analysis/results/cachewise-tb-timeout-stability-20260731/result.json; post-hoc attribution in research-directions-20260729.md.

## Slide 16
IMPLICATIONS · TAKEAWAYS · NEXT STEPS
结论：停止 tuning；下一次证据必须跨过 task 与真实压力两道门
16
① insight survives
相对 next-reuse ordering 是正确 systems objective；tool metadata 确实含 tail signal。
② estimator fails
whole-args、progress、synthetic SWE、exact timeout 都未通过稳定 gate。
③ scope matters
offline regret 不是 eviction/JCT；TB aggregate pass 也不能覆盖 single-task fragility。
NEXT EVIDENCE RUNG
freeze current NO-GO
no post-hoc clause/text rescue
→
new independent tasks
task-grouped gate; environment-scale hypothesis
→
task-stable ranker
charge inference + scheduling overhead
→
live KV pressure
30–50 sessions; actual evictions + JCT
最终 takeaway
“use tool args” 不是方法贡献；可发表的问题是：什么 inference-time state 能跨 task 稳定改善一个真实、计费完整的 KV decision？
Paper: arXiv:2606.16824v1 · Local source index: analysis/offline/related-work.md and analysis/development/research-directions-20260729.md.